## Slide 1: Application of Data Programming Blocks
MODULE 2

## Slide 2: Objectives
 Understand the use of data programming blocks and their applications
 Understand the basic logic operations and apply them in programming robots.
 Perform mathematical operations using the math block.
 Control switches/loops using range and compare blocks
 Create variables and constants.
 Use the random block to personalize your robot

## Slide 3: Data Blocks
In this module we are going to study the configurations & applications of each block.

## Slide 4: Math Block
The Math Block is used to perform a mathematical operation on two input integer numbers.
The result of the operation is available on an output data plug.
The math operations are addition, subtraction, multiplication, and division.
Using the math block, you can calculate the area of an object, the total distance travelled by the robot or modify a sensor reading to reflect the score in a pinball game
Used to Calculate absolute value and square root.

## Slide 5
Math Block
Operation
Output (Result)
Input
Numbers
Configuration Panel
Data Block
A and B values can either be manually set in the configuration panel Or dynamically set with input data wires.

## Slide 6: Variable Block
The variable block stores and retrieves variable values.
You can save sensor readings in a variable and then update them after performing mathematical operations.
For Example, you can count the total number of red or blue objects produced in a factory.

## Slide 7
Using variables in NXT-G is a two-step process.
First you create the variable, and then you use the Variable block in your program to work with the data contained in the variable.
Variable Block

## Slide 8
1.To create a variable, go to edit define variables
As you can see in the figure, we created a new variable entitled “NumberVar” with the “Number” Datatype. You can create other data types such as “logic” or “text”.
Variable Block

## Slide 9
2. Next, we can configure a Variable block to either read or write to the NumberVar variable that we created.
Variable Block
Variable Action WRITE
Variable Action
READ
Variable Type

## Slide 10
To do so, use the Configuration Panel to select the variable from the list, and then set the Action item to either Read or Write.
When Read is selected, the variable’s current value is put on the data wire attached to the output data plug.
When Write is selected, a value is stored in the variable. That value can be supplied either using the Configuration Panel or via an input data wire.
Usually, you will need to use the Configuration Panel to set a variable’s initial value at the beginning of a program, and then use a data wire if you want to change the value later in the program.

## Slide 11
This block can take up to three inputs. It determines whether a test number is inside or outside a range of numbers.
It outputs a logic value depending on the result of the comparison.
Range Block
Test Value
Lower Limit
Upper Limit
Output Result
Range Value

## Slide 12
This is the Configuration Panel for the range block. You can set the range by using the two-sided slider, by entering the values in the A and B boxes or by supplying the two range limit values using data wires.
Using the slider, you can aselect lower and upper limits between 0 and 100. To use values greater than 100 or less than 0, enter the numbers in the boxes.
The test value can be entered into the box on the Configuration Panel or supplied by using a data wire.
Using the range block, you can improve on traditional color sorting codes by specifying a range values for each color
Range Block

## Slide 13
Lab Activity 1
Tasks 1 & 2

## Slide 14
This block is designed to perform a logical operation on its inputs and output a true/false logical value.
Its operations consist of , , ,
Logic Block
Logic
Operation
Output Result
Input
conditions
NOT
AND
Xor
OR

## Slide 15
The result of the Or operation will be true if either input value is true or if both input values are true.
The result will be false only if both input values are false.
Example: you want your robot to change direction if the ultrasonic value is less than 20 cm or the touch sensor is pressed.
OR

## Slide 16
The result of the And operation will be true only if both input values are true.
If either input value is false, then the result will be false.
Example: you want your car to operate when the ignition key is ON and all the doors are closed.
AND

## Slide 17
Xor is an abbreviation for Exclusive Or.
This is similar to the Or operation except that the result is false if both input values are true.
Example: you want your robot arm to pick either candy or ice cream but not both.
Xor

## Slide 18
This operation uses only the A input value and generates the opposite value.
If the input value is true, then the output value will be false, and if the input value is false, then the output value will be true.
NOT

## Slide 19
Logical operations are often described using a table that lists all the possible input values and the result for each operation.
This is called a truth table

## Slide 20
1. You select the operation you want to perform.
2. Supply the Input values, using either data wires OR the configuration Panel
Logic Block: Configuration Panel
Buttons are used to set the values in the Configuration Panel, with the (√) meaning true and the (x) meaning false.

## Slide 21
Lab Activity 1
Task 3

## Slide 22
Constant Block is used to access constants in your program.
This block looks like the Variable block, with a lock added to show that the value cannot be changed
Constant Block
Constant Name
Constant Type

## Slide 23
Constant Block: Configuration Panel
The Action item determines how you will define the value to use, either selecting a constant from the list created using the Edit define constants dialog OR creating a custom constant
The Data type can be logic, text or number. You can set the name and the value of the constant block by entering the values in the configuration panel. The name of the constant will be shown on the block
To use the constant value, simply connect a data wire to the Constant block’s output data plug.

## Slide 24
This block simply compares two numbers as to whether or not the first number is greater than, less than, or equal to the second number.
It outputs a logic value depending on the result of the comparison.
Compare Block
Input Numbers
Comparison Operation
Output Result
When the block runs; it takes the two input numbers, compares them, and puts the resulting logic value on the output data wire.
For example, if the A value is 7 and the B value is 12, the result will be true, because 7 is less than 12. On the other hand, if A is 25 and B is 8, the result will be false, because 25 is not less than 8.

## Slide 25
You can supply the two input values using data wires or the Configuration Panel.
Using the compare block, you can compare the readings from two ultrasonic sensors. You can then use the result of the comparison to control a Switch or Loop block to determine which way your robot should go.

## Slide 26
Random Block is used to generate a random number. It takes two inputs in the form of the min and max values of the random numbers it will be allowed to generate.
It is used to create robotic games or a robot that exhibits unpredictable behavior because the block’s output will vary each time the program runs.
Often a robot that is a little unpredictable can be more interesting or seem to have more personality.
Random Block
Lower Limit
Upper Limit
Random Number (Min and Maximum)

## Slide 27
Random Block
Like the range block, you can set the range by using the two-sided slider, by entering the values in the A and B boxes, or by supplying the two range limit values using data wires.
Using the slider, you can select lower and upper limits between 0 and 100. To use values greater than 100 or less than 0, enter the numbers in the boxes. The minimum value for the lower limit is 0 while the maximum value for the upper limit is 32767.

## Slide 28
Lab Activity 2

## Slide 29
Review Questions